## Slide 1
Resistive Heating for Cable Solder Flow
September 2020
James Logan

## Slide 2: Concept
Do heating for cable solder flow by driving current through cable
Copy as much existing power electronics, connector designs, calculations, etc. as possible from existing body of work
  Source power supply from same family as WHAM magnet driver
  Copy power supply/cable connectors & related calcs from WHAM magnet driver
  Straight-up copy Dan N’s WHAM solder controller rig to drive solder reservoir heating
Keep it simple
  If it works without insulation, don’t insulate it
  If there are COTS heating elements that work, use them

## Slide 3: Heating Calculations
The cable is modeled as a horizontal copper cylinder in ambient air
  Jacket is modeled as 3mm copper; actual
Natural convection heat losses calculated per Churchill & Chu correlation
Connector resistances estimated as 0.5mOhm per connector
  Per WHAM’s PDR materials for cable connectors for the same power supply (slide 97)

## Slide 4: Performance Estimates – 25V, 2kA Supply
Looks good uninsulated out to about 150m cable length
This covers
  Short-section dev cables
  CSMC
  SPARC
Would need insulation to do PF coils
Bump times are typically <10% of solder flow time
Calculations (excel & jupyter): https://www.dropbox.com/sh/kz3p1is6b2mf0i0/AABi30b9gEivslBp9s_yAvEqa?dl=0

## Slide 5: Open Items
Connectors need active cooling
  ~9kW dissipation per connector at max current
  Likely have to throw away end-sections of cable due to uneven heating
  Might need to do better than 0.5mOhm cables/connectors to decrease losses
Hot-spotting in copper cable
  Independent of solder wetting, there will be some length-wise variation in resistivity
  1% variation in resistivity -> ~1% difference in power dissipation, but if it’s a short section, that will conduct upstream and downstream
  Unclear what “normal” lengthwise resistivity variation will look like
How much wattage can we pull?
  Need at least ~25kW
B-fields and hoop stresses for coil geometries
  Is it ok to put this much current into those coils? How much support is needed? Can the supports be thermally insulated effectively?
Composites compatibility – do we have to do this before wrapping coils?

## Slide 6: BOM (W.A.G.)
Item | $ (tot) | Count | Description
MagnaPower TSDx-xxxx/480 | ~$12,000 | 1 | High-current power supply, likely 25V/2000A
4550T121 | $236 | 4 | 4ft, 312W heater tape (for solder reservoir)
WHAM solder controller | $1,432 | 1 | 4p4t temperature controller (for solder reservoir)
BX-DM1E-10ED13-D | $777 | 1 | PLC w/ ethernet, 6ch RTD module, analog output module, & all terminal blocks
PLC software (DataWorx) | $400 | 1 | Only one PLC needed for small workpieces
RTDs for cable sense | ~$300 | 4 | Guestimate for short cables
High-current cables & connectors | ~$1,000 | 2 | Guestimate
Total | $16,145 |  | 
Magna-Power Catalog: https://magna-power.com/assets/files/datasheets/datasheet_ts_4.4.0.pdf
WHAM solder controller: https://www.dropbox.com/home/SPARC_Joint/Research_Projects/GDT/Manufacturing/Heating%20Ring

## Slide 7: Assumptions
Target temperature is 200C; ambient temperature is 20C
Radial thermal diffusion >> convective rate -> lumped-parameter model is valid
  Bi = hD/k = 3e-4 to 7e-4, Biot number agrees
Cable core internal geometry not important to heat transfer at jacket surface
  Seems ok. In reality, will get slightly less heat transfer between jacket-core lands
Solder electrical conductivity is negligible
  Leaded solder typically <=10% of copper’s electrical conductivity
  In bare configuration (with convection), conservative to assume section wetted w/ solder to run colder by about the atmospheric temp delta times the dissipative power ratio
    180K * P_wetted / P_dry = 180K * R_wetted / R_dry since the same current flows through both
    In reality, convective heat transfer also decreases linearly with surface temp, so temp delta will be less
  This gives a worst-case temp delta of about 1-2K if solder takes up ~5-10% of cross-section
Copper resistivity corresponds to 200C temperature (about 2x ambient)

## Slide 8: BACKUP

## Slide 9: Magna-Power Stock Model Catalog
Magna-Power Catalog: https://magna-power.com/assets/files/datasheets/datasheet_ts_4.4.0.pdf

## Slide 10: Solder Flow Velocity 1/3
Stated values are longitudinal velocity – flow velocity relative to channel walls is slightly faster
Evaluated using B-N-T approximation for friction factor
  This gives an explicit formulation that extends across turbulent transition
  Confirmed gives same result as Haaland for high Re as-implemented
  https://ascelibrary.org/doi/10.1061/%28ASCE%29HY.1943-7900.0001540
Assumed channel geometry is 0.3mm x 5.5mm at 20cm pitch (14 deg angle) w/ 10% relative roughness
  Helical path length bookkept as increased wetted length; no accounting for minor losses which should be small due to inability to develop counter-rotating vortex in thin passage
Downstream pressure assumed vacuum
Did not account for non-flowing deadspace, which seems likely to increase actual flow times by ~2-3x
Liquid 60-40 solder properties per matweb (2cP viscosity, 8600 kg/m^3)
  http://www.matweb.com/search/datasheet_print.aspx?matguid=06a31d97bb734b509043d81cf131b280

## Slide 11: Solder Flow Velocity 2/3

## Slide 12: Solder Flow Velocity 3/3